## Slide 1: Risk based targets as new tools for risk management
Moez SANAA
Microbial Risk Assessment and Mitigation Workshop:
towards a Quantitative HACCP Approach
Dubai February 23, 2012

## Slide 2: Opportunities for the Food Business operators
Risk based concept provides targets for the cost-effective design of FSM systems in individual businesses
  Flexibility in combining the relative effects of control measures
  Moving away from reliance on analytical testing (high operational costs) towards reliance on validation (increased cost of product development)
Reduces barriers to international trade
  Provide adequate documentation of compliance with ALOPs (or ALOP – derived targets) at different markets
  Provides documentation of equivalence, despite diverging national legislation

## Slide 3: Technically, equivalence to pasteurization does not exist !
Pathogen | Pasteurisation 72 °C, 15 sec | High Pressure Treatment (500 Mpa, 21.5 °C, 10 min)
L monocytogenes | 11.8 | 10-11
S. aureus | 6.6 | 3-4
E. coli O157:H7 | 41.9 | 1-2
Log reductions achieved by alternative treatments of milk:
Data provided by Claus Heggum

## Slide 4: What we mean by equivalence?
Equivalence (Equusvalere= same value): Different means and measures that lead to the same result or outcome Equivalence in food safety formally recognized by:
  •WTO in 1995 (SPS agreement)
  •EU in 2002 (Food Law)
  •Codex in 2003 (RM principles)
Only option is to benchmark against QUANTIFIABLE OUTCOMES according to the principle of equivalence

## Slide 5: Achieving equivalent outcomes
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6
Process 1 | 5 | 6 | 1 | 3 | 2 | 0.5
Process 2 | 2 | 2.2 | 2.2 | 3.7 | 2.7 | 1
Log CFU/ml
Desired outcome before sale
Point of compliance
Point of Equivalence
Time or steps in the process

## Slide 6: MRM metrics definitions
Food Safety Objective:“The maximum frequency and/or concentration of a hazard in a food at the time of consumption that provides or contributes to the appropriate level of protection (ALOP)”
Performance Objective (PO):“The maximum frequency and/or concentration of a hazard in a food at a specified point in the food chain before the time of consumption that provides or contributes to an FSO or ALOP, as applicable”
Performance Criterion (PC):“The effect in frequency and/or concentration of a hazard in a food that must be achieved by the application on one or more control measures to provide or contribute to a PO or FSO”

## Slide 7: MRM metrics definitions
Process Criterion (PrcC):The processing conditions that must be met to achieve the PO/PC
Product Criterion (PrdC):The characteristic(s) of a food that must be maintained or achieved to achieve a PO/PC/FSO
Microbiological Criterion (MC):The level and/or frequency detected by a specified method and sampling plan that achieves the PO/PC

## Slide 8: FSO/PO/MC
Establishing a FSO or a PO is both a scientific and a societal decision
  FSO is means of relating stringency of the entire farm-to-table system to public health outcomes
  PO is the primary means of articulating the level of stringency to level of performance at a specified step in the food chain
  MC is a means of verifying that a PO is being achieved

## Slide 9
Consumption
Storage
Retailing
Transport
Conditioning
Step 4
Step 3
Step 2
Step 1
Reception
Transport
Harvest
Step 5
Preparation
Cooking
FSO
ALOP
PO1
PO2
PO3
PC
PC
PC
PrC
PrC
PrC
PC
PdC
Food Safety Objective
Performance Objective
Performance Criterion
Process Criterion
Product Criterion
Control measures
Control measures
Control measures
Control measures
Microbial Criteria

## Slide 10: Available frameworks
Quantitative risk assessment (QRA)
  Governmental task
  Intended to support of generally targeted risk management decisions (e.g. mitigation through law)
  Modeled scenarios much broader than one food from one manufacturer (i.e. enormous variation)
Quantitative hazard analyses within the HACCP context
  Food business task
  Intended to document safety of a “plant/product/intended use” combination
  Modeled scenarios specific to each plant & process line (i.e. variation is limited and often well-known)
  Quicker & less costly than QRA

## Slide 11: Traditional HACCP approach
Implemented in many food businesses as a QA system and not as a risk-based management system
  The flow diagram provides the structure for the hazard analysis
  ”Hazard” is understood as ”something that can go wrong”(e.g. “microbial growth”, “post contamination”)
  Focus is on whether the CCPs are in control
  The CCPs are often identified among those control measures that were in place beforehand
Traditional HACCP systems tend to be focused on avoiding unlucky accident in the operation of processing steps

## Slide 12: What is needed?
A shift in focus:
  Hazards as agents - not as mishaps
  Control of the hazard levels – not of the control measures
  Hazards to be considered individually – not as a group(s)
  Each batch has it’s own unique food chain
Quantitative food safety outcomes (max hazard levels)
Tools and data that enable the FBO to document confidence in the manner each hazard is controlled from farm to fork.

## Slide 13: Wher we are kno?
The risk-based metrics (FSO, PO and PC) are ready for operational implementation
  ISO 22000 provides a HACCP framework that fits better than the Codex framework
  Codex provides the necessary guidelines on validation
  Governments and industry still struggle with the concept
    It is significantly different from traditional approaches
    It is difficult to communicate
    Implementation requires new scientific knowledge, new software-based tools and additional skills
BUT:
  Knowledge, tools & skills do already exist to allow different companies to start utilizing the opportunities in practice
  Growing awareness of the benefits (increased reliability, cost-reduction and operational freedom) will drive developments

## Slide 14: The metric-Driven hazrad analysis
1. Prelimineray Steps
2. Hazards Identification
3. Hazards Assessment
4. Selection of control measures
5. Metrics for the control measures
(PCs) and additional (POs)
6. Validation of control measure combination
7. PrCs and PdCs for the measures
8. Control of control measures and system verification
PRPs
POs for end products

## Slide 15: Selection of control measures Outcome from the hazrad analysis
If higher than the PO
Reduction of levels is needed
Alternatives, for instance:
  Lower initial levels in raw materials and/or ingredients
  Reduced contamination (improved PRPs)
  Reduced time and/or temperature at storage steps and/or shelf life
Permits, for instance:
  Raw materials and/or ingredients with higher levels
  Less stringent PRPs
  Increased time and/or temperature at storage steps and/or shelf life
If lower than the PO
Room for less stringent control

## Slide 16: The metric-Driven hazrad analysis
1. Prelimineray Steps
2. Hazards Identification
3. Hazards Assessment
4. Selection of control measures
5. Metrics for the control measures
(PCs) and additional (POs)
6. Validation of control measure combination
7. PrCs and PdCs for the measures
8. Control of control measures and system verification
PRPs
POs for end products

## Slide 17: Establishing metrics for the control measures
PCs for essential control measures
  Processing steps necessary for making the product, and during which hazard levels change significantly
  Microbiocidical step(s) that can achieve the required reduction
Additional POs
  Raw materials
  Ingredients
Validation of the capability to deliver the Pos for end products
  Literature reviews
  Regulations
  Challenges studies
  Statistical analysis of data obtained during normal operation
  Predictive modeling
Corresponding process criteria and/or product criteria
  Literature reviews
  Regulations
  Challenges studies
  Predictive modeling

## Slide 18: Major application
Demonstration of compliance with micro criteria without doing analytical testing
Determination of (safety) shelf life
Comparison of the relative effect of two/more control measures
Implementation of new technology
Designing the control systems and documenting safety of raw milk cheese
Ranking pathogens to identify which are the most decisive for the safety of the food
Design of the entire hazard control system for key hazards
Determining the need for microbiocidal treatments
Determining the extent of acceptable growth at specific steps
Establishing acceptance criteria for incoming materials
Optimizing means and frequency of verification activities

## Slide 19: Example